## Slide 1: A Probabilistic Seismic Hazard Model for Sub-Saharan Africa
Valerio Poggi1, Graeme Weatherill1, Julio Garcia1, Marco Pagani1
R. Durrheim2, G. Mavonga Tuluka3, A. Nyblade4
1 - Global Earthquake Model (GEM), Pavia Italy
2 - University of the Witwatersrand, Johannesburg, South Africa
3 - Goma Volcanic Observatory, DR Congo
4 - Penn State University, USA
June 29, 2016, Addis Ababa - Ethiopia

## Slide 2
Introduction and Motivation

## Slide 3: Introduction
The East African Rift System (EARS) is the major active tectonic feature of the Sub-Saharan Africa (SSA) region
Several past large earthquakes caused a non-negligible level of damage
A reliable risk assessment is therefore essential, which requires a state-of-art hazard assessment for the region
We propose an new probabilistic seismic hazard model for SSA based on the most recent and up to date available information

## Slide 4: GEM’s Philosophy
The Sub-Saharan Africa Hazard Model (as for all GEM products) is meant to be:
1) Collaborative
Although the initial pilot model has been proposed by GEM, we promote its development through collaboration between scientists from African institutions and worldwide
2) Open and transparent
All input information (e.g. catalogue), data (configuration files) and results are openly accessible to the community for verification, improvement or any use

## Slide 5: GEM – SSA Hazard Model
Presently available PSHA Model Components:
  Earthquake Catalogue
    Agency Selection
    Magnitude Homogenization
    Declustering
  Source Zonation
  Seismicity Analysis (for area sources):
    Completeness & MFD Parameters
    Depth Distribution
    Source Mechanism
    Rate Balance
  GMPE Selection
  Logic Tree Implementation & Uncertainty
  PSHA Calculations & Results

## Slide 6
The new SSA Earthquake Catalogue

## Slide 7: Merging Earthquake Catalogues
Input Catalogues:
ISC-REV
ISC-GEM
GCMT
GEH
AfricaArray
Agency Selection
Agency Prioritization
Tanzanian Broadband Seismic Experiment (TZB)
Ethiopian Plateau Catalogue (ETP)
AfricaArray Eastern Africa Seismic experiment (AAE)

## Slide 8: Magnitude Homogenization
Examples

## Slide 9: SSA Earthquake Catalogue
GSHAP
NEW!
29803 events
3 ≤ Mw ≤ 7.53

## Slide 10: SSA Catalogue Declustering
We use Gardner & Knopoff (1974) algorithm
7259 events out of the original 29803 (3 ≤ Mw ≤ 7.5)
To obtain estimates of stationary seismicity rates the recurrence models need to be fit to earthquake catalogues that are purged of non-Poissonian Events (i.e. foreshocks and aftershocks) which are dependent

## Slide 11: Accessing Relative Agency Contribution
DECLUSTERED
SSA CATALOGUE
Were AfricaArray data of any significance?
YES, but not for seismicity analysis…..
AfricaArray
Data Integration

## Slide 12
Area Source Zonation

## Slide 13: Area Source Zonation
GEM - Version 6.0
GSHAP
Based on:
Previous studies
Seismicity
Surface Faults
Plate boundaries
Strain models

## Slide 14: Source Groups

## Slide 15: Multiple Layer Strategy
Zone XX.00
Zone XX.01
Overlapping Layer
Background Layer
Calibration Layer
An overlapping layer inherits the characteristics (completeness, b-value, source geometry) of the background
Rates are redistributed by keeping the total rate balance unmodified

## Slide 16
Source Parameters

## Slide 17: Depth Solution Distribution
Fix-Depth Solutions Removed
Final
Statistic
Uncertain
Large-Depth
Solutions Removed





## Slide 18: Source Mechanism Statistic
Bibliographic information + open datasets
Strike Distribution
Fault Style
(Dip+Rake)

## Slide 19: Catalogue Completeness Analysis
Regional Threshold
Source Group 5
comp_table = [[4.50, 0.25, 1967., 2013.],
[4.75, 0.25, 1967., 2013.],
[5.00, 0.25, 1967., 2013.],
[5.25, 0.25, 1967., 2013.],
[5.50, 0.50, 1951., 2013.],
[6.00, 0.50, 1901., 2013.],
[6.50, 1.00, 1901., 2013.]]
First, a regional completeness analysis was performed
Source groups have been subsequently refined to account for spatial variability
Alternative methods (e.g. Stepp, 1997) were also tested
Regional Threshold
SSA Full Catalogue

## Slide 20: MFD – Seismicity Analysis
Using a truncated Gutenberg- Richter magnitude occurrence relation with
Mwmin = 4.5
SSA Full Catalogue
Source Group 4
New strategy based on direct inversion of observed incremental occurrences rates
Not affected by data correlation
Bins of arbitrary width / completeness
Either a, b or Mwmax can be fixed

## Slide 21: MFD – Seismicity Analysis
Group | a | b | Mwmax
1 | 5.4629809325 | 1.0233537813 | 7.2
2 | 4.7012917208 | 0.9472904903 | 7.5
3 | 4.6964659876 | 1.0215313804 | 6.9
4 | 5.4566139474 | 1.0154006974 | 7.9
5 | 4.9062300341 | 0.9914650334 | 6.9
6 | 5.7370738808 | 1.1585298966 | 7.4
Could be improved using strain models!
The b-values were kept constant within source groups, while the rates have been calibrated separately for each source zone
Rates have been redistributed between overlapping layers by preserving the total balance of the zone
Maximum magnitude was defined based on the maximum observed magnitude for the zone, plus about 0.5 magnitude units

## Slide 22
Logic Tree Implementation

## Slide 23: GMPE Selection - Introduction
Given the unfortunate lack of calibration recordings, GMPE selection can only be made based on general considerations about:
The tectonic context of validity
Type and quality of data used for calibration
Suitability of the functional form
However, African regions interested by the rift system are in a quite peculiar seismotectonic setting
Seismicity can hardly be classified as just of stable continental or active shallow type, but hybrid behavior might be expected

## Slide 24: GMPE Selection – Weighting Strategy
Chiou & Youngs (2014)
Akkar et al. (2014)
Atkinson & Boore (2006)
Pezeshk et al. (2011)
 Active Shallow Crust
 Stable Continental Crust
We have selected four suitable GMPEs, two per seismotectonic setting:
Four main tectonic categories have then been identified, which allows the assignment of different weight combinations to the GMPEs

## Slide 25: GMPE Selection – Mapping GM Variability
Distance Scaling
Magnitude Scaling
The selection was performed with the goal of best representing the epistemic variability of the ground motion models

## Slide 26: GMPE Selection – Comparing Spectra
Distance (rjb)
Magnitude

## Slide 27: Source Parameter Uncertainty - Regionalization
We only considered uncertainty on Mmax
What about other sources of uncertainty?

## Slide 28
PSHA Results using OpenQuake Engine

## Slide 29: Hazard Calculation Using OpenQuake
The Sub-Saharan Africa Hazard model has been calculated for:
2722 sites (about 50km resolution), 192426 ruptures
2% and 10% PoE in 50 Years (R.P. of 2474 and 474 years, respectively)
Outputs: hazard curves, uniform hazard spectra (UHS), hazard maps
Spectral periods: PGA, 0.05s, 0.1s, 0.2s, 0.5s, 1s and 2s
Statistic: mean hazard and percentiles (0.15, 0.5 and 0.85)
Rock reference conditions (Vs30=600m/s); no site-specific response
6.3 hours on 256 cores

## Slide 30: Hazard Curves @ African Capitals
Ethiopia
Kenya
Uganda
Burundi
10% POE in 50 years
0.2s

## Slide 31: Uniform Hazard Spectra @ African Capitals
Ethiopia
Kenya
Uganda
Burundi
10% POE in 50 years
0.2s

## Slide 32: Hazard Maps @ PGA
10% POE in 50 years
2% POE in 50 years

## Slide 33: Hazard Maps @ 0.05s
10% POE in 50 years
2% POE in 50 years

## Slide 34: Hazard Maps @ 0.2s
10% POE in 50 years
2% POE in 50 years

## Slide 35: Hazard Maps @ 1s
10% POE in 50 years
2% POE in 50 years

## Slide 36: Moving Forward
Although SSA Hazard model has been finalized, several issues still remain open…
Missing PSHA Model Components:
  Fault Models  Information is fragmented; how to proceed?
  Strain Rates  Strain model already available, but not used so far
  Strong Motion Data  AfricaArray, IRIS?
  Alternative Seismicity Models  Smoothed Seismicity?
  Disaggregation Scenario  Focusing on major cities? Ongoing…..
  Site-specific response  Possible microzonation studies?
Food for thought…

## Slide 37
  Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-nd/3.0/
  Please attribute to the GEM Foundation with a link to
  www.globalquakemodel.org
Thank you!